## DMC-G4  Diesel Fire Pump Controllers				      MASTER

---------- EQUIPMENT ORDERED ----------

COMPLETE CONTROLLER MODEL NO.

IN TYPE 2 DRIP PROOF ENCLOSURE (OR AS INDICATED BELOW)

FOR USE WITH       VDC       GROUND SYSTEM FOR TWO BATTERY UNITS

EACH HAVING (QTY)       TYPE       CELLS WITH MAX. CAPACITY SHOWN BELOW

INPUT POWER       VAC AT       HZ.  SINGLE PHASE       AMP MAX.

(BRANCH CIRCUIT REQUIRED.  15 AMP BRANCH IS ADEQUATE).

ENGINE MAKE            ENGINE MODEL

##### MODEL

DMC	– 12 VDC, NEG GROUND, 115 VAC			 DMC – 24 VDC, NEG GROUND, 115 VAC

DMC – 12 VDC, NEG GROUND, 230 VAC			 DMC – 24 VDC, NEG GROUND, 230 VAC

INCLUDES MODIFICATIONS CHECKED BELOW:

(CONTROLLER MODEL NUMBER INDICATES MODIFICATIONS SUPPLIED)

POC – PROGRAMMABLE OPTION CHASSIS – PROVIDES 8 PROGRAMMABLE INPUTS AND 8 PROGRAMMABLE

RELAY OUTPUTS.   CONTACTS ARE RATED 6 AMPS AT 30 VDC, 6 AMPS AT 250 VAC.  UL PILOT DUTY

RATINGS R300  AND B300.  RELAYS CAN BE PROGRAMMED FOR ANY OF THE FOLLOWING:  AUTO OFF,

BATTERY FAILURE, CHARGE FAILURE, ELECTRONIC ENGINE ALARMS (301-304, 310-312), FAILURE TO

START, HIGH WATER, LOCKOUT, LOW DISCHARGE PRESSURE, LOW FUEL, LOW OIL, LOW SUCTION

PRESSURE, LOW ZONE (ON DEMAND), OVER PRESSURE, OVERSPEED, PUMP HOUSE TROUBLE, PUMP

RUN, START CONTACTOR FAILURE, TRANSDUCER FAILURE.

FC     – FOAM CONTROLLER				 15A   – 300 PSI, 300 SERIES SS PRESSURE TRANSDUCER,

L        – ADDS 18" PAINTED  LEGS TO CONTROLLER		   TEST VALVE SOLENOID & WET PARTS

8E     – CE DECLARATION FOR EUROPEAN COMM.	 16A   – 500 PSI, PRESSURE TRANSDUCER, TEST VALVE

3R     – TYPE 3R RAINTIGHT ENCLOSURE		   	   SOLENOID & WET PARTS

4       – TYPE 4 WATERTIGHT ENCLOSURE		 19      –  SPACE HEATER

4XB – TYPE 4X, 304 SS WATERTIGHT ENCLOSURE	 20      –  SPACE HEATER WITH THERMOSTAT

4XC – TYPE 4X, 316 SS WATERTIGHT ENCLOSURE	 20A   –  SPACE HEATER WITH HUMIDISTAT

12      –TYPE 12 DUSTTIGHT ENCLOSURE		 32      –  LOW PUMP ROOM TEMPERATURE SWITCH

12B   – ADDS 36" NEMA 12 BASE CABINET FOR 		 83LT –  LOW SUCTION TRANSDUCER & WET PARTS

72" HEIGHT

15     – 300 PSI, 316 SS PRESSURE TRANSDUCER

TEST VALVE SOLENOID & WET PARTS

,

ORDER ALSO INCLUDES:

4817 – LOW FUEL SWITCH (SHIPPED LOOSE FOR FIELD INSTALLATION)

4817L – LONG ROD LOW FUEL LEVEL SWITCH (FOR LARGER DIAMETER OR TALL TANKS)

6288 – HIGH FUEL SWITCH (SHIPPED LOOSE FOR FIELD INSTALLATION)

REMOTE ALARM PANEL       FOR REMOTE INSTALLATION AT A POINT OF CONSTANT ATTENDANCE

JOB IDENTIFICATION:

| Master Control Systems, Inc. LAKE BLUFF, ILLINOIS U.S.A | DMC ORDER SELECTION DRAWING | Date: 24 July 2019 |
| --- | --- | --- |
|  |  | Drawing 22399 Issue 2 |